## Slide 1: COST-REVENUE DOMINATED CASH FLOW

## Slide 3
Cost Dominated Cash Flow
OUTFLOWS (+VE)
Investment
Expenditure
INFLOWS
(-VE)
Profit
Revenue
Salvage Value

## Slide 4
Revenue Dominated Cash Flow
OUTFLOWS
(-VE)
Investment
Expenditure
INFLOWS
(+VE)
Profit
Revenue
Salvage Value

## Slide 10: Production engineers of a manufacturing firm have proposed a new equipment to increase productivity of manual gas cutting operation. The initial investment is Rs 5,00,000 and equipment will have a salvage value of Rs 1,00,000 at the end of its expected life of 5 years. Increased productivity will yield an annual revenue of Rs 2,00,000 per year. If the firm’s minimum attractive rate of return is 15%; is the procurement of new equipment economically justified? Use Present worth, Annual Equivalent and Future Worth Method.

## Slide 11: GIVEN:- P= -5,00,000 F= 1,00,000 N=5 YEARS i= 0.15 A= 2,00,000 REVENUE BASED

## Slide 12: PW= -P + F P + A P

## Slide 13: PW= -5,00,000 + 1,00,000 (P/F, 0.15,5) + 2,00,000 (P/A, 0.15,5) = 2,20,160 > 0 It is economically justified.

## Slide 14: FW= -P F + F + A F

## Slide 15: FW = -5,00,000 (F/P, 0.15,5) + 1,00,000 + 2,00,000 (F/A, 0.15,5) = 4,42,500 > 0 It is economically justified.

## Slide 16: AW= -P A + F A + A

## Slide 17: AW = -5,00,000 (A/P, 0.15,5) + 2,00,000 + 1,00,000 (A/F, 0.15,5) = 65,653.79525 > 0 It is economically justified.

## Slide 18: Investment proposals A and B have the net cash flows as given in the table. Compare the Present worth of A with that of B at i=18%. Which proposal should be selected?
PROPOSAL | 0 | 1 | 2 | 3 | 4
A | -10,000 | 3000 | 3000 | 7000 | 6000
B | -10,000 | 6000 | 6000 | 3000 | 3000

## Slide 19: For A: P=-10,000 R=0.18 F1=3000 F2=3000 F3=7000 F4=6000 FOR B: P=-10,000 R=0.18 F1=6000 F2=6000 F3=3000 F4=3000 REVENUE BASED

## Slide 20: PW(A)= -10,000 + 3000(P/F, 0.18, 1) + 3000(P/F, 0.18, 2) + 7000(P/F, 0.18, 3) + 6000(P/F, 0.18, 4) = Rs 2052.10

## Slide 21: PW(B)= -10,000 + 6000(P/F, 0.18, 1) + 6000(P/F, 0.18, 2) + 3000(P/F, 0.18, 3) + 3000(P/F, 0.18, 4) = Rs 2767.40 . B will be selected.

## Slide 22: A granite company is planning to buy a fully automated granite cutting machine. If it is purchased under installment basis, the company has to pay 25% of the cost (cost = Rs 16,00,000) at the time of purchase and the remaining amount in 10 annual equal installments of Rs 2,00,000 each. Suggest the best alternative for the company using present worth basis at i=18%

## Slide 23: P= 4,00,000 A=2,00,000 R=0.18 N=10 COST BASED

## Slide 24: PW= 2,00,000 (P/A, 0.18,10) + 4,00,000 = Rs 12,98,820 second option is selected.

## Slide 25: A finance company advertises two investment plans. In plan I, company pays Rs 12,000 after 15 years for every 1000 invested now. In plan II, for every Rs 1000 invested now, the company pays Rs 4000 at the end of 10th year and Rs 4000 at the end of 15th year. Select the best alternative plan from investor’s point of view by using present worth amount. (i= 12%)

## Slide 26: Plan l: P= -1000 F=12,000 R=0.12 N=15 Plan II: P= -1000 F1= 4000, N=10 F2= 4000, N=15 R=0.12 N=15

## Slide 27: PW: -1000 + 12,000(P/F, 0.12,15) = Rs 1192.40 PW: -1000 + 4000(P/F, 0.12,10) + 4,000(P/F, 0.12,15) = Rs 1018.8 Plan 1 is selected.

## Slide 28: A man owns a corner flat. He must decide which of the several alternatives to select in trying to obtain a desirable return on his investment. After much study and calculations, he decides that the two best alternatives are as given below. Which one will be selected based on Future worth analysis? (i= 12%)
 | Build gas station | Build soft ice-cream stand
First cost | 20,00,000 | 36,00,000
Annual Property Tax | 80,000 | 1,50,000
Annual Income | 8,00,000 | 9,80,000
Life | 20 | 20

## Slide 29: A(Build gas station)= 8,00,000-80,000= 7,20,000 A(Build soft ice-cream stand)= 9,80,000- 1,50,000 = 8,30,000 Revenue based
 | Build gas station | Build soft ice-cream stand
P | 20,00,000 | 36,00,000
A | 80,000 | 1,50,000
A | 8,00,000 | 9,80,000
N | 20 | 20

## Slide 30: FW(Build gas station)= -20,00,000(F/P, 20,0.12) + 7,20,000 (F/A, 20,0.12) = Rs 3,25,85,440

## Slide 31: FW(Build soft ice-cream stand)= -36,00,000(F/P, 20,0.12) + 8,30,000 (F/A, 20,0.12) = Rs 2,50,77,560

## Slide 32: M/S Krishna Casting Ltd. Is planning to replace its annealing furnace. It has received tenders from three different original manufacturers of annealing furnace. The details are as follows: (i= 20%). Which one will be selected based on Future worth analysis?
Manufacturers | 1 | 2 | 3
Initial Cost | 80,00,000 | 70,00,000 | 90,00,000
Life | 12 | 12 | 12
Annual Maintenance Cost | 8,00,000 | 9,00,000 | 8,50,000
Salvage Value | 5,00,000 | 4,00,000 | 7,00,000

## Slide 33: Cost based
Manufacturers | 1 | 2 | 3
P | 80,00,000 | 70,00,000 | 90,00,000
N | 12 | 12 | 12
A | 8,00,000 | 9,00,000 | 8,50,000
F | 5,00,000 | 4,00,000 | 7,00,000

## Slide 34: FW(Alternative 1)= 80,00,000 (F/P, 12,0.20) + 8,00,000 (F/A, 12,0.20) - 5,00,000 = Rs 10,24,92,800

## Slide 35: FW(Alternative 2)= 70,00,000 (F/P, 12,0.20) + 9,00,000 (F/A, 12,0.20) - 4,00,000 = Rs 9,76,34,900

## Slide 36: FW(Alternative 3)= 90,00,000 (F/P, 12,0.20) + 8,50,000 (F/A, 12,0.20) - 7,00,000 = Rs 11,31,87,850

## Slide 37: A Company is planning to purchase an advance machine centre. Three original manufacturers have responded to its tenders whose particulars are tabulated as follows. Which one will be selected based on Annual Equivalent Worth analysis?
Manufacturers | Down payments | Yearly equal installments | Number of Installments | Rate of Interest (%)
1 | 5,00,000 | 2,00,000 | 15 | 20
2 | 4,00,000 | 3,00,000 | 15 | 20
3 | 6,00,000 | 1,50,000 | 15 | 20

## Slide 38: COST BASED
Manufacturers | P | A | N | I
1 | 5,00,000 | 2,00,000 | 15 | 20
2 | 4,00,000 | 3,00,000 | 15 | 20
3 | 6,00,000 | 1,50,000 | 15 | 20

## Slide 39: AE(Alternative 1)= 5,00,000 (A/P, 15,0.20) + 2,00,000 = Rs 3,06,950

## Slide 40: AE(Alternative 2)= 4,00,000 (A/P, 15,0.20) + 3,00,000 = Rs 3,85,560

## Slide 41: AE(Alternative 3)= 6,00,000 (A/P, 15,0.20) + 1,50,000 = Rs 2,78,340